## Slide 1: Module 5: Area Scanner Programming
PLC Tabletop Training Program · Hands-on Lab · 2.5 h
v1.0 (April 2026)

## Slide 2: Learning objectives
Program or verify the configuration of an Omron OS32C area scanner
Define protective and warning zones using the OS32C Configuration Tool
Confirm OSSD outputs are functioning correctly via PLC monitoring
Physically verify zone boundaries with measurement

## Slide 3: Overview
Programming and verifying the Omron OS32C area scanner — defining safety zones, configuring OSSD outputs, and physical verification.

## Slide 4: Lesson: OS32C Configuration Tool Setup
Installing the tool, connecting via USB, and reading existing configurations

## Slide 5: OS32C Configuration Tool Setup (content)
→ Install the Configuration Tool
Download the OS32C Configuration Tool from Omron's website. Requires Windows 10/11.
→ Connect to the Scanner
• Connect a USB cable from your laptop to the mini-USB port on the OS32C
• Open the Configuration Tool and select the correct COM port
• Click Connect
• Click Read from Device to load the current zone configuration
The configuration tool shows the scanner's detection field as a top-down polar view. Existing zones appear as colored overlays.

## Slide 6: Lesson: Defining Safety Zones
Creating protective and warning zones, configuring detection parameters

## Slide 7: Defining Safety Zones (content)
→ Zone Types
Table: Zone | Purpose | Response
• Protective Zone | Immediate danger area around the machine | OSSD outputs drop immediately — machine stops
• Warning Zone | Approach area outside the protective zone | Warning output activates (alarm, slow-down) but OSSD stays active
→ Defining Zone Boundaries
• Select the zone type to edit (protective or warning)
• Draw the zone boundary using the polygon or radius tool in the configuration software
• Set the detection sensitivity (minimum object size) — typically 30–70mm for personnel detection
• Configure multiple zone sets if the machine requires different safety zones for different operating modes
• Download the configuration to the scanner and verify the new zones are active

## Slide 8: Defining Safety Zones (content)
[WARNING] Zone Validation Required: After any zone change, you must physically verify the boundaries. Walk toward the scanner from multiple angles and confirm the protective zone triggers at the correct distance. Measure with a tape measure and compare to the configured boundary.

## Slide 9: Lesson: OSSD Testing & Verification
Confirming safety outputs are properly wired and functioning

## Slide 10: OSSD Testing & Verification (content)
→ OSSD Verification Procedure
• With the scanner configuration active, confirm both OSSD1 and OSSD2 outputs are wired to the PLC safety input or safety relay
• Open the PLC software and go online — monitor the safety input tags mapped to the OSSD outputs
• With the zone clear, verify both OSSD tags show TRUE (both channels active)
• Have a person enter the protective zone — verify both OSSD tags drop to FALSE simultaneously
• Remove the person from the zone — verify both OSSD tags return to TRUE
• Confirm the downstream safety circuit responds correctly (machine enabled/disabled)
[DANGER] Single-Channel Failure Test: If your safety system allows it, test single-channel failure: temporarily disconnect one OSSD wire. The safety relay should detect the channel disagreement and lock out. If the machine continues to run on one channel only, the safety wiring is incorrect and must be fixed immediately.
→ Scanner LED Status
Table: LED State | Meaning

## Slide 11: OSSD Testing & Verification (content)
• Green steady | Normal operation — zone clear
• Yellow steady | Warning zone intrusion detected
• Red steady | Protective zone intrusion — OSSD dropped
• Red flashing | Scanner fault or configuration error

## Slide 12: Lab: USB Connection & Live Scan View
After: OS32C Configuration Tool Setup
Duration: 10 min
Connect USB to the OS32C on the bench. Open the configuration tool and show the live scan view. Have students walk at various distances to see themselves in the scan display.
Students walk toward and away from the scanner, watching the detection point move in real time. Makes the concept of detection zones tangible.

## Slide 13: Lab: Zone Programming & Physical Verification
After: OSSD Testing & Verification
Duration: 15 min
Modify a warning zone boundary, download to the scanner, then physically verify with a student approaching. Show the OSSD output state change on the PLC dashboard simultaneously.
Students measure actual trigger distance with a tape measure and compare to configured distance. Verify both scanner LED and PLC input state change.

## Slide 14: Quiz
What happens when an object enters the protective zone of an area scanner?
A warning alarm sounds but the machine continues | The OSSD outputs drop and the machine stops | The scanner displays an error message | Nothing — the operator must press E-stop

## Slide 15: Quiz
After changing zone boundaries in the configuration tool, what must you do?
Just click Save and the scanner updates automatically | Download to the scanner AND physically verify the new boundaries with measurement | Reboot the PLC | Replace the scanner batteries

## Slide 16: Quiz
The area scanner's LED is flashing red. What does this mean?
Normal operation — zone is clear | Warning zone intrusion | Scanner fault or configuration error | Low battery