## Slide 1: Module 6: HMI Navigation & Fault Clearing
PLC Tabletop Training Program · Lecture + Lab · 2.5 h
v1.0 (April 2026)

## Slide 2: Learning objectives
Log into an HMI screen and navigate between key screens
View and interpret active alarms and fault history
Clear faults and reset the machine after a safe condition is restored
Use the I/O status screen to verify field device communication
Manually jog or operate outputs for maintenance testing

## Slide 3: Overview
Operating the HMI screen — login, alarm management, I/O status monitoring, and fault clearing procedures.

## Slide 4: Lesson: HMI Overview & Login
What an HMI is, screen navigation, and user access levels

## Slide 5: What is an HMI?
HMI stands for Human-Machine Interface. It's a touchscreen panel that lets the operator monitor and control the PLC system in real time. Common brands on site: Omron NB/NA series, Allen Bradley PanelView, AutomationDirect C-more.

## Slide 6: Logging In
Touch the screen to wake it — the home/overview screen will display
Look for a padlock icon, user icon, or "Login" button (typically upper-right corner)
Enter credentials using the on-screen keypad (check machine binder for default maintenance credentials)
Press Enter or OK to log in

## Slide 7: User Access Levels
Table: Level | Typical Users | Permissions
Operator | Production operators | View status, clear minor alarms, start/stop cycles
Maintenance | Maintenance technicians | View I/O status, clear faults, manual jog, adjust setpoints
Engineering | Controls engineers, automation lead | Full access — modify screens, change configurations, adjust safety parameters

## Slide 8: Lesson: Alarm Management & Fault Clearing
Reading alarms, understanding fault codes, and restoring normal operation

## Slide 9: Viewing Active Alarms
Navigate to the Alarms screen (often a bell icon or dedicated Alarms button). Active alarms display the alarm code, description, timestamp, and associated tag name. Most recent alarms appear at the top.

## Slide 10: Fault Clearing Procedure
Read the alarm — note the alarm code, description, and timestamp. Take a photo for documentation.
Identify the root cause — use the alarm description and tag name to determine what triggered the fault. Open PLC software if needed to trace the associated logic.
Correct the physical condition — clear an obstruction, replace a sensor, reset a safety device, fix a wiring issue. Never clear an alarm without addressing the cause.
Clear the alarm on the HMI — select the alarm and press Clear/Reset. Some alarms require the fault condition to be gone before they can be cleared.
Verify normal operation — confirm the alarm doesn't immediately return and the machine enters Ready state.
[DANGER] Never 'Clear and Hope': Clearing an alarm without fixing the underlying cause is a recipe for recurring faults, production downtime, and potential safety incidents. If the alarm comes back after clearing, the root cause hasn't been resolved.

## Slide 11: I/O Status Screen
The I/O status screen shows real-time states of all inputs and outputs. Use it to verify sensors are communicating, outputs are energizing, and the physical world matches what the PLC reports.

## Slide 12: Lesson: Manual Control & Setpoint Adjustment
Jogging outputs, testing devices, and adjusting parameters from the HMI

## Slide 13: Manual Jog/Output Control
During maintenance, you may need to manually operate individual outputs — jog a motor, extend a cylinder, energize a solenoid — for testing or positioning. This is done from the HMI's Manual Control screen (maintenance access required).
[WARNING] Safety First: Manual mode bypasses the normal automatic sequence. Ensure the area is clear, safety guards are functional, and all personnel are aware before jogging any output.

## Slide 14: Setpoint Adjustment
Timers, counters, speed references, and recipe parameters can be adjusted from the HMI. Always note the original value before changing it. Changes take effect immediately on most systems.

## Slide 15: Lab: Live HMI Walkthrough
After: HMI Overview & Login
Duration: 10 min
At the bench HMI, log in, navigate to key screens: overview, I/O status, alarms, manual control. Activate a proximity sensor and show the I/O status screen reflect it.
Each student navigates to a different screen on the HMI. Students confirm they can find the I/O status screen and identify physical device states.

## Slide 16: Lab: Fault Injection → Alarm → Clearance
After: Alarm Management & Fault Clearing
Duration: 15 min
Trainer creates a fault (blocks area scanner). Walk through: read alarm → identify cause → clear obstruction → clear alarm → verify normal operation.
After trainer demo, each student performs the full cycle: trainer injects a fault → student reads alarm → fixes physical cause → clears alarm → verifies.

## Slide 17: Quiz
What is the correct order for clearing a fault on the HMI?
Clear the alarm first, then investigate the cause | Read the alarm → Identify and fix the root cause → Clear the alarm → Verify normal operation | Restart the PLC → Clear all alarms → Resume production | Call the supervisor and wait

## Slide 18: Quiz
The HMI shows three access levels. What can a Maintenance-level user do that an Operator cannot?
View production statistics | Access I/O status, clear faults, manual jog, and adjust setpoints | Modify HMI screens | Nothing — they have the same access

## Slide 19: Quiz
An alarm appears on the HMI. You clear it, but it immediately returns. What does this mean?
The HMI is malfunctioning | The root cause of the fault has not been resolved | You need to restart the PLC | The alarm has a 5-minute timeout