## Slide 1: Module 8: Advanced Manufacturing Specifics
PLC Tabletop Training Program · Lecture + Discussion · 3.5 h
v1.0 (April 2026)

## Slide 2: Learning objectives
Locate and use custom build documentation for Vermeer machines
Understand core ladder logic instructions and their symbols
Configure basic servo motor parameters in Sysmac Studio
Create and use global variables with proper naming conventions
Add I/O modules and devices to an existing PLC configuration

## Slide 3: Overview
Custom machine documentation, ladder logic building blocks, servo motor configuration, global variables, and adding I/O components to a PLC.

## Slide 4: Lesson: Custom Machine Documentation
Where to find documentation for Cobot Carbide Tower, Cobot Reamer, Servo Motor, and Rodloader

## Slide 5: Custom Machine Documentation
All custom build documentation is stored on the shared network drive under: Engineering > Custom Builds > [Machine Name]. Always check here first before making any changes.
Table: Machine | Key Documents
Cobot Carbide Tower | Wiring diagrams, Omron NX1P2 PLC program, Sysmac Studio project file, robot cell layout. Check revision history for latest approved version.
Cobot Reamer | Task program, EtherCAT slave configuration, tooling offset table, safety zone drawings.
Servo Motor Incorporation | Axis mapping spreadsheet, drive parameter backup file, mechanical coupling specs, motion profile documentation.
Rodloader | Full wiring package, Productivity Suite project, I/O assignment list, sequence of operations document.
[WARNING] Revision Control: Always verify you are working from the latest revision. Outdated documentation leads to incorrect troubleshooting and wasted time.

## Slide 6: Lesson: Ladder Logic Building Blocks — Part 1
Core instructions: contacts, coils, latches, timers, and counters

## Slide 7: Contacts and Coils
Table: Instruction | Symbol | Function
Normally Open (XIC/NO) | --[ ]-- | Passes power when the referenced bit is ON (1). Checks if an input is active.
Normally Closed (XIO/NC) | --[/]-- | Passes power when the referenced bit is OFF (0). Blocks logic when a fault/interlock is active.
Output Coil (OTE) | --( )-- | Sets the referenced bit ON when the rung has power. Turns OFF when power is lost.
Latch (OTL) | --(L)-- | Sets the bit ON and it stays ON even after the rung loses power. Requires an unlatch to turn off.
Unlatch (OTU) | --(U)-- | Turns off a latched bit. Used in pairs with OTL for start/stop logic.

## Slide 8: Timers
Table: Timer | Function | Common Use
TON (Timer On-Delay) | Starts counting when rung is true. DN bit turns ON after preset time. | Debounce sensors, sequence delays, dwell times
TOF (Timer Off-Delay) | Starts counting when rung goes false. DN bit stays ON for preset time after rung goes false. | Cooldown periods, coast-down timing
RTO (Retentive Timer) | Like TON but accumulator retains value when rung goes false. Must use RES to reset. | Total run-time tracking, accumulated process time

## Slide 9: Counters
Table: Counter | Function | Common Use
CTU (Count Up) | Increments by 1 each time the rung transitions from false to true. DN bit turns ON at preset. | Part counting, cycle counting
CTD (Count Down) | Decrements by 1 each transition. DN bit turns ON when accumulator reaches zero. | Batch remaining count, magazine count

## Slide 10: Lesson: Ladder Logic Building Blocks — Part 2
Comparison, math, move instructions, and other function blocks

## Slide 11: Comparison Instructions
Comparison instructions evaluate two values and pass power if the condition is true:
Table: Instruction | Meaning | Example
EQU | Equal | Check if counter = target value
NEQ | Not Equal | Check if status flag has changed
GRT | Greater Than | Check if temperature exceeds limit
LES | Less Than | Check if pressure is below minimum
GEQ | Greater Than or Equal | Check if timer accumulator >= setpoint
LEQ | Less Than or Equal | Check if speed is within range

## Slide 12: Math & Move Instructions
MOV (Move): Copies a value from Source to Destination. Used for loading setpoints, copying recipes, and resetting accumulators.
ADD / SUB / MUL / DIV: Arithmetic on tag values. Used for scaling analog signals, calculating rates, and batch arithmetic.
CPT (Compute): Evaluates a formula expression. Useful for complex calculations in a single instruction.

## Slide 13: Lesson: Servo Motor Configuration
Setting up servo axes in Omron Sysmac Studio over EtherCAT

## Slide 14: Adding a Servo Axis
In the Sysmac Studio project tree, go to Motion Control > Axes
Right-click and add a new Servo Axis
Assign it to the EtherCAT node number matching the physical drive (check drive's rotary switches or DIP settings)

## Slide 15: Unit Conversion Settings
Under Axis Parameters > Unit Conversion, configure:
Encoder pulses per revolution
User units (mm, degrees, inches) per motor revolution
Gear ratio if a gearbox is present

## Slide 16: Key Parameters
Table: Parameter | What It Controls | Risk if Wrong
Max Velocity | Speed limit for the axis | Too fast = mechanical damage, too slow = cycle time loss
Acceleration / Deceleration | Ramp rates | Too aggressive = motor faults, too gentle = slow response
Position Limits | Software travel limits | Prevents axis from moving beyond mechanical range
Torque Limit | Maximum motor force | Too high = potential to damage tooling or workpiece
[WARNING] Parameter Changes on Production: Never change servo parameters on a production machine without comparing to the documented values first. Small changes to acceleration or position limits can cause crashes, product damage, or injury.

## Slide 17: Lesson: Global Variables & Adding Components
Creating global variables, naming conventions, and adding I/O modules

## Slide 18: Creating Global Variables
Global variables are accessible from any program block in the PLC project. In Omron Sysmac Studio, define them in the Global Variable Table. In Allen Bradley Studio 5000, these are Controller-scoped tags.

## Slide 19: Naming Convention
Use a function area prefix for instant clarity:
SAFETY_ — E-stop, safety relay, scanner signals
MOTION_ — Servo axis commands and feedback
HMI_ — Operator interface signals
CONV_ — Conveyor system signals
IO_ — General I/O points

## Slide 20: Adding I/O Components
Table: Platform | Steps
Omron (EtherCAT) | Right-click EtherCAT master > Add Slave. Select from ESI library. Assign node address. Map tags to I/O channels in the I/O Map view.
Allen Bradley | Right-click I/O Configuration > New Module. Search by catalog number. Set IP address and slot. Download and verify in I/O tree.
AutomationDirect | Use the I/O Configuration wizard in Productivity Suite. Select module type, assign slot, map tags.

## Slide 21: Lab: Servo Parameters — Live Adjustment
After: Servo Motor Configuration
Duration: 15 min
On the EtherCAT servo drive, show current parameters. Make a safe change (reduce velocity by 50%), command a move, observe the difference. Restore original.
Students read parameters, predict what a change will do, observe the result, then restore. Reinforces the read → predict → verify → restore cycle.

## Slide 22: Lab: Add I/O Component End-to-End
After: Global Variables & Adding Components
Duration: 15 min
Walk through adding a new tag for an unused I/O point: create tag, map to physical channel, write a simple rung, download, test with physical device.
Students follow along on laptops, replicating the tag and rung. Each pair tests their logic on the bench — the capstone integrative activity.

## Slide 23: Quiz
A TON timer has a preset of 5000ms and the accumulator shows 5000ms. Is the DN (Done) bit ON or OFF?
OFF — the timer is still counting | ON — the accumulator has reached the preset | It depends on the rung state | OFF — 5000ms means the timer has reset

## Slide 24: Quiz
What is the difference between OTE (Output Coil) and OTL (Output Latch)?
They are the same | OTE turns off when the rung loses power; OTL stays on until an OTU unlatch instruction | OTL is faster than OTE | OTE is used for digital, OTL for analog

## Slide 25: Quiz
Before changing servo motor parameters on a production machine, what should you do?
Just make the change — parameters auto-revert on restart | Compare the current values to the documented values and backup the program first | Switch the PLC to PROGRAM mode | Disconnect the encoder

## Slide 26: Quiz
What prefix would you use for a global variable controlling an E-stop circuit?
CONV_ | MOTION_ | SAFETY_ | HMI_